Main Feature:

- 1.3MP@25 fps;

- High sensible and IR enhanced SONY sensor;

- High permeable /resolution glass fisheye lens with 185° horizontal/vertical field of vision;

- High sensible and low noise pickup system;

- Omni-directional IR Illumination;

| Specification | YSJ-HF-TA2201 |
| --- | --- |
| Optoelectronic |  |
| Lens | Fisheye lens, f=1.29mm, F=2.2 |
| Field of Vision | Horizontal 185°/Vertical 185° |
| Iris | Fixed |
| Sensor | 1/3" Progressive Scan CMOS |
| Sensibility | 0.2Lux@F2.2(Color)/0.02Lux@F2.2(B/W) |
| Day/Night | Auto switch IR cut |
| IR Illumination | 1W@850nm |
| Image |  |
| Image Flip | Horizontal/Vertical |
| Image Adjustment | Brightness, Saturation, Sharpness, Contrast, Tone |
| Max. Resolution | 1.3 Megapixels（1280×1024） |
| Video Coding | Dual Stream H.264 |
| Bit Rate | 100Kbps~5120Kbps |
| Max. Frame Rate | 25fps |
| Audio |  |
| Microphone | Internal |
| Audio Coding | G.711 |
| Pickup Distance | 6 Meters |
| Panoramic Function | Enabled by software |
| Panoramic Display | Support unwrap on ceiling, wall and 支持顶装、壁装和地装等安装模式的投影展开，支持多分割窗口的虚拟摄像机显示 |
| DPTZ | Digital PTZ，Pan/Tilt/Zoom |
| Intelligent Function |  |
| Motion Detection | 20×15 Regional detecting, Sensibility 1~6 adjustable |
| Alarm Function |  |
| Alarm Trigger | Motion Detection/Video Tampering/Abnormal procedure/Alarm Input |
| Alarm Action | Alarm Record/Image Snap， Alarm Video/Image Upload（FTP/Email） |
| Network |  |
| Protocol | TCP/IP，HTTP，DHCP，DNS，RTP/RTSP，FTP，PPPOE，SMTP，NTP |
| Compatibility | ONVIF2.0 |
| Interface |  |
| Communication Port | 1 RJ45 10M/100M Ethernet |
| Power Interface | ø5.5-2.1mm round DC socket |
| Local Storage | Up to 128G SD Card |
| 一般参数 |  |
| Power Supply | DC12V±10%，1A |
| Power Consumption | <6W |
| Working condition | -15℃~+50℃@Humidity 10%~ 95% |
| Storage Condition | -40℃~+75℃@Humidity 10%~ 95% |
| EMC | CE，FCC |
| Housing | PC cream-coloured |
| Protection Grade | IP50 |
| Product Size | Φ100*36.6mm |
| Weight（kg） | N.W.：0.1 / G.W.：0.2 |

# Text boxes

1.3MP Fisheye Panoramic IP Camera YSJ-HF-TA2201