Quick Guide: fisheye panoramic camera

Thank you for choosing our product. If you have any questions about our product, feel free to contact us.

This manual may contain technical inaccuracies, inconsistencies with product’s functions or typographical errors. Our company will update the content of the manual in accordance with the enhancement of our product and renew regularly the product or the software described in this manual. Updated contents will be added in the new version of the manual without further notice.

# Interface and network

# configuration

# quick access

After connecting the camera and a computer into the same local area network (LAN), the computer can control the camera. Set the IP address of the computer to the same as the camera: 192.168.0.※. The default IP address of the camera is 192.168.0.123, user name: admin and password: 123456. After these modifications, use PING command to verify if the computer and the camera can successfully communicate. If not, check power line and network cable to make sure they are properly connected. Computer IP address settings:

The following shows how to access quickly to the camera via IE or Panosee software.

## access to camera via ie

Open IE browser, select “enable” or “prompt” for all the plug-ins in “ActiveX controls and plug-in” of tools-security-custom level(C), set the security level to medium or low.

Enter the IP address of the camera in the address bar, press Enter. If it is the first visit, a control will pop up automatically. Click [Run] to install the control.

After the installation, the network camera will enter the login screen. Input the login password to enter the preview screen.

## Software

Install software from the CD attached. When run the software after installation, a wizard will pop up if it is an initial entry, select the device that need to be added, click [add].

Select an online device, click [add] to add it. When successfully added, click [exit wizard] to exit and to enter the preview screen.